## Slide 1: T200 Thruster How To
Reef_Engineer
5/15/2024

## Slide 2: Products Used
Arduino Uno R4 Wifi - $40
  Currently requires servo library update to work correctly. R3 and under work correctly out of the box.
  Optional case for Arduino
Blue Robotics T200 ($200) or T500 ($690) Thruster
  I used T200, very large tanks would benefit from T500 (it is 3x the power). I do not have a thruster housing print file for T500, just T200. The T500 does have improved wear/corrosion features.
  You can request one from Blue Robotics with a 3m cable instead of the stock 1m cable, good for keeping electronics box far from water.
Blue Robotics ESC (Basic $40, Basic 500 $110)
  Need different for T200 and T500 so choose the correct one. T200 uses Basic ESC and the T500 uses Basic ESC 500. ESC is what powers the thruster using signal from the microcontroller, and power from the power supply.
DROK Power supply ($70)
  Power supply with adjustable current and voltage, displays both. Allows you to feed your ESC up to 20V.
Potentiometer 10K Ohms ($10 for 3)
  Used to control speed/max speed of the thruster in the program, read by the Arduino
3 Way Switch ($9 for 2)
  Used to select drive mode for the thruster, read by the Arduino
Misc Electronic Wires and connectors needed
Fan to cool ESC
Electronics Box
Low voltage connector cables
Pass through connectors
Power cable
  16 gauge grounded power cable, brings power into the electronics box attaches to power supply
Low voltage connector kit (if you don’t already have any of these)
Magnets – need 6 of them (BE CAREFUL THEY ARE VERY STRONG)
I don’t have links to them, but some felt sheet to go between magnet mount and outer glass, and silicone sheet to go between thruster housing and inside glass.

## Slide 3: Electronics Box In/Out
Controls
  Potentiometer knobs (2)
    Only 1 needed for 1 thruster right now
  Mode Selection Switch
    3 Positions
    Would need another if running 2 Thrusters
  T200 Power Cable
    Need 2 for 2 Thrusters
  120V Power Cable

## Slide 4: Wiring Diagram
120 V grounded power line
  Runs into housing, wired to input of power supply
  Power supply programmed to deliver 0-20V to the power rail
  Keep track of positive and negative sides of the power rail!
  BE CAREFUL – this is exposed 120V here – deadly
  The power rail is jumped so three sets per side are pos and three sets negative
  The ESC and Arduino can take 8-20V. The T200 will run like crazy at 20V. I think they suggest 16V max, many people run them at 8V. Start low.

## Slide 5: Wiring Diagram
Power Rail
  I attached this to the top of the power supply
  Power coming to rail is adjustable Voltage from supply 0-20V
  Arduino needs 5-20V
  ESC needs 8-20V (start low)
  Could also power blower fan from here directly, but I run it off of Arduino 5V
Negative Power from Supply
Negative Power to Arduino
Negative Power to ESC
Positive Power to Arduino
Positive Power to ESC
Positive Power from Supply

## Slide 6: Wiring Diagram
ESC Wiring
  Gets power from Rail -, +
  Black wire is ground (connect to Arduino Ground)
  White wire is PWM signal from Arduino (connect to Pin 9)
  Blue/Green/White wires are three phases of power to the Thruster. I matched colors but it doesn’t really matter, reversing two of them will reverse thruster direction

## Slide 7: Wiring Diagram
Arduino Wiring
  Power coming from rail to Arduino via barrel connector
  (1) Ground and (2) Pin 9 to ESC
  (3) Ground, (4) 5V, and (5) A0 (signal) to Potentiometer
  (6) Ground, (7) Pin 7, and (8) Pin 8 to Mode Switch
  (9) Ground, (10) 5V to FAN
Arduino is in case and epoxied to the top of the power supply
1
2
3
4
5
6
7
8
9
10

## Slide 8: Wiring Diagram
Wires to Back Wall of Box
  3 Way Switch
    Middle is ground from Arduino
    Left is Pin 7 from Arduino (Ramp Up/Down)
    Right is Pin 8 from Arduino (Random Flow)
  Potentiometer
    Wired as indicated on previous slide to Arduino
  T200 Power out (top right)
  120V Power In (bottom Right)

## Slide 9: Resources
YouTube video of Assembly
Arduino program
Housing 3D print files